## Slide 1
SOLAR PV INDUSTRY
IN 2025
Alan Xu, 2015.11
45th APEC EGNRET Meeting,
Xiamen China, Nov. 18th, 2015

## Slide 2
A leading solar company with the most prudent operation
    Proven project development track record and 9.2 GW project pipeline
    Strong bankable brand with global reach
Best product warranty backed by investment grade insurance policy
Founded in Ontario, 2001
Listed on NASDAQ (CSIQ) in 2006
  Over 8,600 employees globally
Global footprint in 90 countries
2014 Shipment
3.1 GW
2014 Revenue
2.96 Billion
2015 Shipment Guidance
4.0~4.3 GW
Accumulated modules, projects and systems sales above 12 GW
Top Solar Company in The World
2

## Slide 3
Singapore
Sales Subsidiary
Madrid, Spain Sales Subsidiary
Munich, Germany EMEA Headquarters
London, UK Sales Subsidiary
Ankara, Turkey Sales Team
Guelph, Canada
Global Headquarters
Australia Sales Subsidiary
Tokyo, Japan Subsidiary
Suzhou, China Subsidiary
Seoul, South Korea Sales Subsidiary
Thailand
Sales Subsidiary
Johannesburg, South Africa Sales Subsidiary
Framingham, US Sales Subsidiary
San Ramon, US Canadian Solar Inc.
Abu-Dhabi
Sales Subsidiary
Brazil,
Sales Subsidiary
India
Sales Subsidiary
Philippines
Sales Subsidiary
Chile,
Sales Subsidiary
Vietnam
Module Factory
Panama
Sales Subsidiary
Global Network for Production, Sales & Service
3

## Slide 4
Abstract
The shortage of energe resources and environmental pollutions have been calling a global energy transition, to be sustainable and to be clean. PV energy completely suits these both requirements. And the history of PV industry has proven to the world that PV energy has the capability to push this change
Technology innovations has significantly cut the LCOE of PV generation, and the reduction of costs will continue in the future due to the development of new technologies, intelligent manufacturing, increasing produciton scale, government incentives and so on. Therefore, PV application domain will expand at a even more rapid pace
China has been a giant in both PV production and application. With the direction of “Intelligent PV Manufacturing 2025”, Chinese PV industry sets the whole sale grid parity as the goal by 2025 to provide the public with clean and intelligent energy at a fair price

## Slide 5: Table of Contents
Benefits of PV Energy
Developments in PV Technologies
Outlook and Development
Developments within the Chinese PV Industry

## Slide 6
Solar Energy is Infinite
173,000TW ~ 6 million tons per second, Standard Coal
5 billion years vs. < 150 years , the proven reserve of Coal
Source: World Energy Outlook_2014_International Energy Agency
Amount
Longevity
1.1 Renewable & Clean

## Slide 7
Energy Payback Period is Short
621 kWh (260 W silicon module, 2012 )
Energy Consumed
Energy Produced
 | Irradiance Region I | Irradiance Region II | Irradiance Region III
The Gross Generation in a Life Cycle | 12241 kWh | 9728 kWh | 7956 kWh
Annual Generation | 490 kWh | 389 kWh | 318 kWh
Energy Payback Period | 1.25 years | 1.6 years | 2.0 years
Source: Carbon footprint report_2012_Intertek
1.1 Renewable & Clean
Notes: 一类地区：3200-3300 小时；二类地区：3000-3200；三类地区：2200-3000小时

## Slide 8
Carbon Emission is Low
Energy Industry, the largest source of GHG emissions, 69%
Source: Carbon Footprint Report_2012_Intertek
Pressure to be Green
One Solution
PV power generation, carbon emission, only 2.5% of Coal power
Source: CO2 Emissions Overview_2012_International Energy Agency
Chart: 
| Si PV module | Coal
 | 22 | 955
1.1 Renewable & Clean

## Slide 9
Installation Expanded at a High Speed
2009~2014, the global solar module installation, 30GW/year
Chart: Cumulative Installed PV Capacity in GW
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Cumulative Installed PV Capacity in GW | 1.3 | 1.6 | 2.1 | 2.6 | 3.7 | 5.1 | 6.7 | 9.2 | 15.8 | 23.2 | 40.3 | 70.5 | 100.5 | 138.9 | 178.9
Source: Global Market Outlook for Photovoltaics 2014-2018_2014_ EPIA
1.2 Fast Growing

## Slide 10
Feed-in-Tariff Dropped Dramatically
2005~2015, Feed-in Tariff in Germany decreased 80%, 43 8.7 ct/kWh
Source: Current and Future Cost of PV_2015_Fraunhofer ISE
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | Wind onshore | New fossil
Feed-in Tariff (ct/kWh) | 43 | 40.5 | 38 | 36 | 32 | 29 | 22 | 19 | 11.5 | 9.5 | 8.7 | 9.1 | 10.5
80%
Chart: 
| Wind Onshore | New Fossil
min | 5 | 5
length | 4.1 | 6
1.2 Fast Growing

## Slide 11
Development Potential is Unlimited
2013,
Germany
China
Source: Levelized Cost of Electricity Renewable Energy Technologies_2013_Fraunhofer ISE
< 0.12 € / kWh
( 1450-2000 kWh/m2a,
All PV power plant types )
0.059 € / kWh
( 2000 kWh/m2a,
Utility-scale power plants )
2030,
0.043~0.064 €/kWh
(High solar irradiation)
2025,
whole sale grid parity
1.2 Fast Growing

## Slide 12: Table of Contents
Benefits of PV Energy
Developments in PV Technologies
Outlook and Development
Developments within the Chinese PV Industry

## Slide 13: Table of Contents
Benefits of PV Energy
Developments in PV Technologies
1. Crystalline Silicon Technologies
2. Thin Film Technologies
3. Concentrator PV Technologies
4. Other Technologies
90%

## Slide 14
Modified Siemens Process Technology
Significantly Cut the Costs — silicon material
Expanded reactor accommodates more pairs of rods
Low-temperature hydrogenation replaces high-temperature hydrogenation
Power consumption 75%， One-time conversion rate 5%
Source: GCL New Energy
Key technology, improved, based on the traditional Siemens method
 | Low-temperature hydrogenation | High-temperature hydrogenation
Operating pressure | 2.5~3.0 MpaG | 0.6 MpaG
Operating temperature | 500~550℃ | 1250℃
Reaction principle | Si + 3SiCl4 + 2H2 = 4SiHCl3 | SiCl4 + H2= HCl + SiHCl3
Power consumption | 0.8~1.2 kWh/ kg·Tcs | 3.5~4.5 kWh/kg·Tcs
One conversion rate | 25% mol | 15~20% mol
2.1 Crystalline Silicon Technologies

## Slide 15
Fluidized Bed Rector Manufacturing Technology
will Continue to Reduce the Costs — silicon material
Simple process, low investment, low power consumption and low operation costs
Over 95% one-time conversion rate for silane gas
High recycling rate of main reacting materials
Continuous operation of FBR and thus higher production efficiency
Source: GCL New Energy
A more recent alternative technology, producing granular polysilicon
Silicon particles
2.1 Crystalline Silicon Technologies

## Slide 16
Modified High-Efficiency Ingot Casting Technology
Greatly Increased the Quality — silicon wafer
Similar energy consumption, but much better quality
Lower density of defects, thus higher conversion efficiency of solar cells
Source: GCL New Energy
Improved technology based on polycrystalline ingot casting process, with homogeneous or heterogeneous seeds to optimize the wafers’ grain structures
Traditional poly wafer
High Efficient poly wafer
2.1 Crystalline Silicon Technologies

## Slide 17
Diamond Wire Saw Slicing Technology
will Bring a Substantial Decline to Costs — silicon wafer
Advantages (vs. traditional slurry-based cutting technology):
Faster cutting speed, 2-3 times
More stable production, less cutting waste
More uniform thickness, less surface damage
Mainstream for mono wafer, but poly wafers cut by this technology are incompatible with current mainstream cell processes
A wafer cut by diamond wire
A wafer cut by slurry
2.1 Crystalline Silicon Technologies

## Slide 18
2009~2015, the average annual efficiency increase rate, 0.4%/year ; This rate will continue, tracking the development of technology and the implementation of intelligent manufacturing
2.1 Crystalline Silicon Technologies
sheet resistance rose from 60ohm/sqr to 90ohm/sqr
the width of fine grid lines decreased from 80um to 40um
the number of main grid lines increased from 3 to 4
the quality of silicon improved much
MCCE, PERC........
Chart: 
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Mono | 0.1715 | 0.1781 | 0.1823 | 0.1881 | 0.1902 | 0.1932 | 0.198 | 0.202 | 0.206 | 0.21 | 0.214 | 0.218 | 0.222 | 0.226 | 0.23 | 0.234 | 0.238
Poly | 0.1602 | 0.1622 | 0.1651 | 0.1703 | 0.1731 | 0.179 | 0.183 | 0.187 | 0.191 | 0.195 | 0.199 | 0.203 | 0.207 | 0.211 | 0.215 | 0.219 | 0.223
Efficiency has Made a Big Rise — cell

## Slide 19
Traditional Poly
P
Mono
P
Nano texture black silicon +PERC P
Nano texture black silicon
P
18.0%
~
18.3%
18.5%
~
18.7%
19.3%
~
19.5%
19.5%
~
19.8%
Mono + PERC
P
Mono + IBC
N
Mono + HJT
N
20.5%
~
20.7%
22%
~
23%
Short term
Medium and long term
22%
~
23%
Future Developments of Cell Technologies — cell
2.1 Crystalline Silicon Technologies

## Slide 20
Nano Texture Black Silicon Technology — cell
2.1 Crystalline Silicon Technologies
At the end of 2014, Canadian Solar was the first to realize its industrialization production
Advantages (vs conventional texturing technology):
Lower reflectivity, higher current and increase in efficiency by 0.5%
No longer a problem for diamond wire sawn wafers
Better low-light performance
A wafer textured by conventional tech
A wafer textured by nano
texture black silicon tech

## Slide 21
Passivated Emitter Rear Contact Technology — cell
2.1 Crystalline Silicon Technologies
Two-sided passivation, reducing the surface recombination velocity on the back side
Advantages (vs passivation only on the front surface):
Lower minority carrier recombination rate, larger output voltage
Higher back surface reflection, larger output current
Poly cells (nano texture black silicon + PERC) reach efficiency of 19.3% - 19.6% in mass production, mono PERC cells reach efficiency of 20.5% - 20.8%

## Slide 22
2.1 Crystalline Silicon Technologies
With electric contacts on the back side, increasing sunlight absorption on the front surface
Advantages (vs conventional cells with electric contacts on both surfaces):
No shadowing on the front surface of cells, larger output current
Bigger percent of back electrode contact area, smaller series resistance
Mass production efficiency is expected to reach 22.0% - 23.0%, and laboratory efficiency above 25.0%
Interdigitated Back Contact Technology — cell

## Slide 23
2.1 Crystalline Silicon Technologies
A material with different bandgap to silicon, to increase light absorption
Advantages (vs silicon homojunction cells):
Wider absorption band
Larger output current and voltage
30% higher power output in desert areas per year
Mass production efficiency reaches 22.0-23.0%, laboratory efficiency reaches 25.6%
Si-Based Heterojuction Technology — cell

## Slide 24
2.1 Crystalline Silicon Technologies
PERC technology will be the winner, followed by IBC and Si-HJT
Chart: 
| 2014 | 2015 | 2017 | 2019 | 2022 | 2025
BSF | 0.89 | 0.81 | 0.66 | 0.43 | 0.305 | 0.21
PERC | 0.04 | 0.1 | 0.21 | 0.35 | 0.345 | 0.35
IBC | 0.03 | 0.045 | 0.03 | 0.1 | 0.13 | 0.2
Si-HJT | 0.03 | 0.025 | 0.05 | 0.06 | 0.09 | 0.1
PERT | 0.01 | 0.02 | 0.05 | 0.05 | 0.09 | 0.095
Si-based tandem | 0 | 0 | 0 | 0.01 | 0.04 | 0.045
Si-Based Heterojuction Technology — cell

## Slide 25
2009~2015, the average annual power increase rate of 60-cell crystalline silicon PV modules, 7.5 W/year
This rate will continue, tracking the improvements in cell efficiency
and module component materials
Chart: Power output / W
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Mono | 230 | 235 | 240 | 250 | 260 | 270 | 277 | 284.3 | 291.6 | 298.9 | 306.2 | 313.5 | 320.8 | 328.1 | 335.4 | 342.7 | 350
Poly | 220 | 230 | 235 | 240 | 250 | 260 | 265 | 272 | 279 | 286 | 293 | 300 | 307 | 314 | 321 | 328 | 335
Power has Increased at a Rate of 7.5W/year —module
2.1 Crystalline Silicon Technologies

## Slide 26
Increasing the Automation Level of Production
Helped Improve Quality and Reduce Costs — module
By 2014, module production in China had been experienced 3 stages
“Intelligent PV Manufacturing 2025” will direct the Chinese solar manufacturing processes to the application of information technology and artificial intelligence, thus quality will be further improved and costs be further reduced
2.1 Crystalline Silicon Technologies
Chart: Number of worjers required for 150MW module production lines
| Before 2009 Manual production | 2009~2012 Foreign automation equipment | 2013~2014 Domestic automation equipment
150MW组件生产线所需人员数量 | 306 | 92 | 76

## Slide 27
Next Generation Modules with Double-Glass
Extend the Lifespan to 30 Years — module
Glass sheets in both sides, to meet harsher weather conditions
2.1 Crystalline Silicon Technologies
Advantages (vs modules with polymer backsheet):
Better mechanical performance, more efficient self-cleaning
Stronger resistance to sand and moisture corrosion
Ideal for building integrated PV systems (BIPV)
Superior UV resistance, Lower potential induced degradation (PID)
A longer lifespan of up to 30 years, 21.5% more power output
Chart: 
| Year 0 | Year 1 | Year 2 | Year 3 | Year 4 | Year 5 | Year 6 | Year 7 | Year 8 | Year 9 | Year 10 | Year 11 | Year 12 | Year 13 | Year 14 | Year 15 | Year 16 | Year 17 | Year 18 | Year 19 | Year 20 | Year 21 | Year 22 | Year 23 | Year 24 | Year 25 | Year 26 | Year 27 | Year 28 | Year 29 | Year 30
Regular | 0.97 | 0.97 | 0.963 | 0.956 | 0.949 | 0.942 | 0.935 | 0.928 | 0.921 | 0.914 | 0.907 | 0.9 | 0.893 | 0.886 | 0.879 | 0.872 | 0.865 | 0.858 | 0.851 | 0.844 | 0.837 | 0.83 | 0.823 | 0.816 | 0.809 | 0.802
Double Glass module | 0.975 | 0.975 | 0.97 | 0.965 | 0.96 | 0.955 | 0.95 | 0.945 | 0.94 | 0.935 | 0.93 | 0.925 | 0.92 | 0.915 | 0.91 | 0.905 | 0.9 | 0.895 | 0.89 | 0.885 | 0.88 | 0.875 | 0.87 | 0.865 | 0.86 | 0.855 | 0.85 | 0.845 | 0.84 | 0.835 | 0.83
21.5% more energy output during the life cycle

## Slide 28
Projects of Double-Glass Modules — module
Double-glass modules are the next generation of solar modules
Location: Luoyang, Henan
Completion: August 2008 Canadian Solar’s BIPV power plant
Location: Nanping, Fujian
Completion: December 2014
Canadian Solar’s power plant with double-glass modules
2.1 Crystalline Silicon Technologies

## Slide 29
CIGS Thin Film Technology
The highest efficiency among all thin film technologies, 23.3% in lab
Advantages (vs other thin film technologies):
Less defects in CIGS crystal, more stable performance
A lower degradation rate and a stronger low-light performance
AR coating
ZnO
N-CdS
p- CIGS absorber
Sputtered Mo
Substrate
2.2 Thin Film Technologies

## Slide 30
GaAs Multi-Junction Technology
Lenses and curved mirrors are used to concentrate the sunlight,
Multiple sub cells stack on the top of each other
Advantages (vs other technologies):
Much wider absorption band
Much higher conversion efficiency, 46% when concentrated 297 times
Cell3 （Eg3)
Cell2 （Eg2)
Cell1 （Eg1)
Eg1>Eg2>Eg3
2.3 Concentrator PV Technologies

## Slide 31
Perovskite Thin Film Technology
Efficiency increased dramatically in 5 years , 3.8% 16.2%
Advantages (vs. other technologies):
High extinction ratio
Relatively easy to make the film by spin coating
Less chance for photon induced carriers to recombine
The laboratory efficiency is as high as 20.1%, but not stable
2.4 Other Technologies

## Slide 32: Table of Contents
Benefits of PV Energy
Developments in PV Technologies
Outlook and Development
Developments within the Chinese PV Industry

## Slide 33
Technological Developments are the Cornerstone
The selling price of 320W one-sided modules is 30% higher, but its LCOE is still 10% lower; the more efficiency the back side of bi-facial module contributes, the lower the selling price will be
Chart: 
| 260W one-sided module | 320W one-sided module | 335W bi-facial module 5% from the back | 352W bi-facial module 10% from the back | 368W bi-facial module 15% from the back | 384W bi-facial module 20% from the back | 400W bi-facial module 25% from the back
min | 0.075 | 0.068 | 0.064 | 0.061 | 0.059 | 0.056 | 0.054
length | 0.107 | 0.094 | 0.089 | 0.085 | 0.081 | 0.078 | 0.075
3.1 LCOE will Continue to Decrease

## Slide 34
Intelligent Manufacturing Reduces Production Costs
By now,
The manufacturing level of PV equipment
To 2025,
will lower LCOE even further
Automation development
Artificial intelligence & Information technologies
has effectively reduced manufacturing costs
3.1 LCOE will Continue to Decrease

## Slide 35
Intelligent Manufacturing Reduces Production Costs
By now,
The manufacturing level of PV equipment
To 2025,
will lower LCOE even further
Automation development
Artificial intelligence & Information technologies
has effectively reduced manufacturing costs
3.1 LCOE will Continue to Decrease

## Slide 36
Enlarged Production Scale Reduces LCOE
Solar module prices decrease with the increase of production scale
Source: Current and Future Cost of PV_2015 _Fraunhofer
3.1 LCOE will Continue to Decrease

## Slide 37
Government Incentives will Help Drive Down LCOE
Source: Technology Roadmap Solar Photovoltaic Energy_2014 _IEA
Policy types |  | PV industry needs
1 | Financial policy | Long term, stable low capital cost
2 | Grid connection policy | Simplified grid connection policies and zero connection costs
3 | Approval policy | Simplified approval process and zero approval costs
4 | Land use policy | Well defined and low-cost land use policy
3.1 LCOE will Continue to Decrease

## Slide 38
3.2 The Development of an Energy Internet
will Help Reduce PV Energy Curtailment
The Global Power Grid will be Transformed into
an Energy Sharing Network

## Slide 39
The Intermittency and Volatility of PV Generated
Electricity can be Adjusted and Managed
Source: China 2050 high renewable energy penetration scenario and roadmap study_2050
_ the National Development and Reform Commission's Energy Research Institute
3.2 The Development of an Energy Internet
will Help Reduce PV Energy Curtailment

## Slide 40
The Forecast Data of PV Proportion Goes Up
3.3 Solar PV Power
will Have a Higher Level of Penetration
2010,
IEA
By 2050, the global PV power percentage, 11%
2014,
IEA
In China, it will be 21%
Source: Technology Roadmap Solar Photovoltaic Energy_2014 _ IEA
By 2050, the global PV power percentage, 16%

## Slide 41
All Kinds of Environments and Uses
3.4 PV Applications
will Become Increasingly Diverse
For basic daily energy needs in poor areas
For basic daily energy needs in rich areas
For special energy needs in deserts
LED light charger

## Slide 42: Table of Contents
Benefits of PV Energy
Developments in PV Technologies
Outlook and Development
Developments within the Chinese PV Industry

## Slide 43
4.1 China has Become the PV Leader
in Both Production and Application
A Manufacturing Giant
Since 2007, the Chinese PV industry had been keeping its leading position
Chart: 
| China | USA | Germany | Others
多晶硅产量 百分比 | 0.43 | 0.19 | 0.17 | 0.21
Chart: 
| China | Korea | Japan | Others
百分比 | 0.85 | 0.05 | 0.03 | 0.07
Chart: 
| China | SEA | Japan | Others
百分比 | 0.86 | 0.05 | 0.04 | 0.05
Chart: 
| China | Japan | SEA | Europe | Others
 | 0.74 | 0.06 | 0.06 | 0.06 | 0.08
Source：The Current Status and Outlook of
the Chinese PV Industry_ 2015
_ China PV Industry Association

## Slide 44
The Power of Application
The Chinese domestic market has grown at a surprising pace
Source：The Current Status and Outlook of the Chinese PV Industry
_ 2015 _ China PV Industry Association
Chart: 
| China | Japan | Europe | USA | Australia | Others
百分比 | 0.25 | 0.21 | 0.16 | 0.15 | 0.02 | 0.21
Global PV installation in 2014
4.1 China has Become the PV Leader
in Both Production and Application

## Slide 45
Three Stages of Intelligent Manufacturing in China
Automation, 2005~2015
Completely replace simple manual operations
Partly replace complex manual operations
Lower labor cost and quality cost
Intelligentization, 2015~2020
Intelligentize and interconnect equipments
On-line control production processs
Analyze the data through information and communication technology
Cut quality and management costs
Informatization, 2020~2025
Remotely and centrally control the production process
Collaboratively manage information in the whole industry chain
Cut costs of administration, logistics, service and financing
4.1 China has Become the PV Leader
in Both Production and Application

## Slide 46
New Innovation Systems will be Built
PV Industry
Raw material suppliers
Equipment manufactures
Technology research institutes
Organizations for standardization
Government &associations
Market research instittutes
The government needs to help build an open innovation platform
4.2 Intelligent Manufacturing will Help the
Chinese PV Industry Become Powerful

## Slide 47
Whole Sale Grid-Parity will be Achieved
With the implementation of “Intelligent PV Manufacturing 2025”,
the costs of PV plants will be reduced to RMB 4.0 per Watt
Chart: RMB / W
| PV plant costs 2015 | Module cost reduction with efficiency increase | Material and production cost reduction | Optimization of system and operation costs | PV plant costs 2025
 | 0 | 6.4 | 4.5 | 4 | 0
 | 8 | 1.6 | 1.9 | 0.5 | 4
4.2 Intelligent Manufacturing will Help the
Chinese PV Industry Become Powerful

## Slide 48: Thanks !