APEC Workshop on Advances in Electricity Storage in Support of Distributed Renewable Energy Based Systems
Honolulu, Hawaii, May 10-12, 2004
Dealing with Green Power Intermittency in the Mexican Electrical Sector
Jorge M. Huacuz
Non-Conventional Energy Unit
Electrical Research Institute
Mexico

---
Agenda:
- Introductory Background
- Dealing with Intermittency Model I: Electricity swaps
- Dealing with Intermittency Model II: Concurrent dispatching of wind and hydro
- Concluding remarks

---
The Mexican Power Sector
Fossil fuels: 80%
Large-scale hydro: 12.4 %
Nuclear: 4.8%
Geothermal: 2.7%
Wind & other renewables: <<1%
Total Current Generating
Capacity: 41,177 MW
Two government-owned utilities serve the whole country: 95% grid coverage
Natural gas combined cycle: 34.2%
Other fossil-fuelled: 5.8%
Large-scale hydro + geothermal: 7%
Other renewables: not considered
New Power Requirements
2003-2012: 25,757 MW
Committed: 12,087 MW
Not Committed: 13,670 MW

---
Can Renewables Contribute?
Resource Potential
  - Solar Irradiance: 5 kWh/m2-day, evenly distributed
  - Wind Potential: 5,000-15,000 MW commercially viable now
  - Biomass: Full potential not known. Trash-to-energy: ~ 1,000MW
  - Micro-hydro: Full potential not known. At least 3,500 MW
  - Ocean: Potential not known; ~ 10,000 km of coastline
Applications
  - ~ 2.5 MW grid-connected wind machines
  - ~ 15 MW off-grid photovoltaics
  - ~ 210 MW sugar cane bagasse
  - ~ 8 MW trash-to-energy

---
Green Power Projects
GEF-Assisted:
- Solar assisted combined cycle gas-fired power plant (242/25MW)
- Methane Gas Capture and Landfill Demonstration
- Renewable Energy for Agriculture
- Plan of action for removing barriers to the full-scale commercial implementation of wind power in Mexico
In the Making:
- Small grid-connected photovoltaic systems
- SENER-WB strategic partnership for large-scale implementation of renewables
Other Initiatives
- SENER-IIE Pilot Plan for the development of renewables
- Around 400 MW for private wind power projects

---
Legal, Institutional and Policy Barriers
- Renewables not considered “national assets” by Constitution
- Direct sales to CFE on $/kWh basis, not always competitive
- Distributed green power, at odds with “bigger is better” paradigm:
        Intermittency
        Power quality
        Safety
        Cost
- Regulatory framework needs to improve
- Oil availability, a “mental brake” for change
- Long administrative red tape for new projects

---
Public Electric Service Law
Self supply
  - Electricity produced to satisfy the generator's own needs.
  - No sell to third parties allowed.
  - Creation of self-generating companies with third parties allowed.
  - Surplus electricity can be sold to the grid
  - Electricity swaps with the national utility allowed
Co-generation
  - Joint production of heat and electricity
  - Production of electricity from waste heat
Independent production
  - Electricity generation with no capacity limits
  - For sell to CFE only
  - In compliance with CFE's expansion plans
  - Bidding for least energy cost (US$/kWh)
For self-supply only

---
Right of Access to the Grid
Grid
Local Load
Generador fotovoltaico
Two way
meter
kWh
Wind Farm
Inverter
Interconnection
Point
With the flow
Grid diagram source: CRE Mexico

---
Dealing with Intermittency
Model I: Electricity Swaps

---
Interconnection Contract 09/2001
- Self generator must be legally established entity in Mexico
- Must own generating permit from the National Energy Regulatory Commission
- Installed capacity >0.5MW (solar, wind or small hydro)
- Must sign interconnection contract with national utility
- Must coordinate power delivery with the National Electricity Control Center
- Is entitled to back up power at a cost

---
Reducción de Demanda Pico

---
Interconnection Contract
- Dispatch. Subject to energy availability with the following provisions:
- Electricity Swaps. Based on Total Short Term Cost (Dispatching Cost)
      - Between equal hourly periods
      - Between different hourly periods
      - Between different months along one year
      - Payment for energy not consumed
- Emergency Energy. 1.5 times the applicable tariff
- Complementary Energy. Under contract only
- Ancillary Services. Proportional to plant capacity factor

---
Total Short Term Cost (CTCP)
Least possible price or least possible cost to supply one additional kWh in a given region.
Accounts for:
Transmission restrictions
Grid losses
Offers from other generators
Is based on variable costs:
For fuel
For O&M
Calculated as a marginal cost in $/kWh

---
Swapping Rules
One-to-One compensation between homologous hourly periods
Compensation between different hourly periods according to:
ESP=XSESS=XiESi=XbESb
ES = Surplus Energy X = Compensation Factor
size 12{ ital "ES" rSub { size 8{ ital "pmcomp"} } = { { ital "CTCP" rSub { size 8{ ital "imgen"} } } over { ital "CTCP" rSub { size 8{ ital "pmcomp"} } } } * ital "ES" rSub { size 8{ ital "imgen"} } } {}
size 12{ ital "ES" rSub { size 8{ ital "imcomp"} } = { { ital "CTCP" rSub { size 8{ ital "pmgen"} } } over { ital "CTCP" rSub { size 8{ ital "imcomp"} } } } * ital "ES" rSub { size 8{ ital "pmgen"} } } {}
size 12{ ital "ES" rSub { size 8{ ital "imcomp"} } = { {$"400" ital "MWh"} over {$"300" ital "MWh"} } *"2000" ital "MWh"} {}
size 12{ ital "ES" rSub { size 8{ ital "pmcomp"} } = { {$"300" ital "MWh"} over {$"400" ital "MWh"} } *"2000" ital "MWh"} {}
size 12{ ital "ES" rSub { size 8{ ital "imcomp"} } ="2667" ital "MWh"} {}
size 12{ ital "ES" rSub { size 8{ ital "pmcomp"} } ="1500" ital "MWh"} {}
mgen = month when electricity is generated
mcomp = month when needed electricity is compensated with surplus electricity
Source: CRE Mexico

---
Dealing with Intermittency
Model II: Concurrent Dispatching of Wind and Hydro

---
Rationale
- Good number of small dams for agriculture
- Could be used for electricity generation
- Small capacity Intermittency High $/kWh
- Complementarity of hydro and wind, good prospects:
        - Technically
        - Financially

---
Concurrent Real Time Dispatching
Grid diagram source: CRE Mexico

---
Hourly Complementarity
May
December

---
Monthly Complementarity

---
Concluding Remarks
- Green power intermittency, a major concern for utility engineers:
        - Grid stability
        - System safety
- Electricity swaps ease green power economics, but does not address the main concerns
- Concurrent real time dispatching of wind and hydro could address both concerns
- Further research on both models will continue

---
Instituto de Investigaciones Eléctricas www.iie.org.mx
Thank you…