## Slide 1: CHINA’S Renewable Energy Industrial Development Strategy
Li Junfeng
APEC Renewable Energy Expert Group Meeting
October 13 to 15, 2003
Shanghai China

## Slide 2: Main contents
1.Renewable energy development status
  Resources potential
  Current industrial development progress
  Potential projects
2. 2003-2005 and 2003-2020 RE Industrial Development Strategy
  RE industry development targets
  Development strategy
3. Measures and Actions

## Slide 3: Part 1
Overview of China’s RE industrial development

## Slide 4: Renewable Energy Resources Potentials
Wind 253 GW
Biomass 300MTCE
Solar 0.6MJ/cm2 in Average
Geothermal 6.7 GW
Small Hydro Power 90 GW
Others
Notes: <number>
<footer>
<header>
<date/time>
China has a rich solar energy resource base. Exploitable water power resources is about 378,000 MW, 11% of which has already been exploited. Biomass energy resources, including straw and crop stalks, firewood, and all kinds of agricultural wastes, amount to about 0.26 billion tons coal equivalent, which makes up about 70% of energy used for daily life and about 50% of total energy consumed in the rural areas.

## Slide 5
Wind Resources
Total 250 GW
Mainly located in Northwest, west and the east-coastal region

## Slide 6
Solar Energy
Average radiation is between 3360 to 8400 MJ/m2
2/3 of the territory is above 5020MJ /m2
Richest region is the west part of China, especially Tibetan Plateau

## Slide 7: Current development status for Wind
Wind turbine installation
  28 wind farms have been developed around China
  The largest wind farm is located in Xinjiang, with about 100 MW
  Total installation was 468 MW by the end of 2002
Project investment
  More then 60% the investment from bilateral and multilateral
  Domestic investment is about 40%
Manufacture
  6 manufactures can produce 600 kW system, including 3 joint ventures
  1MW and above system is under the R & D

## Slide 8: Wind turbine installation in China (MW)

## Slide 9: Current development status for solar thermal
More than 1000 manufactures
Annual production is about 10 million m2
Accumulated the largest installation of 33 million m2 by end 2001 in the whole world

## Slide 10: Current development status for solar PV
Installation
  more than 10 MW for household system
  700 village power systems
  more than 20 MW for commercial use
Manufacture
  4 old manufactures with total capacity of 4 MW
  4 new manufactures are under the development stage, at least one is targeted 20 MW production capacity per annual

## Slide 11: Current development status for biomass
Biogas：
  Over 1000 industrial wastewater /livestock farm large-scale biogas engineering
  Annual biogas production 600 million m2
Direct burning of biomass
  90% of the biomass for energy is direct burning for rural households
Other technologies
  improved stove for biomass burning
  Gasification for over 200 village gas systems
  bio-diesel for 10,000 tons per annual

## Slide 12: Current development status for geothermal
Power
  total capacity of 32.08 MW
  mainly in Tibet 25.18 MW
Heatng supply
  traditional heating system about 15 Mm2
  geothermal heat pump systems are increasing like bamboo shoots after a spring rain

## Slide 13: Part 2
2003-2005 and 2003- 2020 Renewable Energy Industrial Development Strategy

## Slide 14: Targets of RE Industry in 2005
By 2005, RE industry development will provide energy about 13 Mtce, equivalent to reduce CO2 10 Mt, SO2 0.6 Mt
Supply power for 1.3 million remote households
Provide 200K employee positions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Targets of RE Sectors
SWH
  Annual production 11 million m2
  Accumulated installations 64 million m2
  Support 5－10 manufacturers
Solar PV
  Annual production 10-15 MW
  Accumulated installations 53 MW
Wind
  Wind farm installation 1000 MW
  Wind turbine production capacity 150-200MW
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Targets of RE Sectors (cont.)
Geothermal
  Space heating area 20 million m2
  Large-scale dissemination of geothermal heat pump technology
Biogas
  Supply 2 billion m3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Industrial Development Strategy
Conform to the guideline to facilitate
  domestic technology
  enterprises’ scale-up
  markets’ regulation
  Products’ standardization
Focus on 4 fields:
  SWH and PV
  Wind
  Biomass
  Geothermal

## Slide 18: 2003-2020 Renewable Energy Industrial Development Strategy
Overall target of RE power generation 100GW
Wind: 20 GW
Small hydro: 50GW
Solar PV: 1GW
Biomass: 15 GW
Others: 14GW
10% of the total capacity by year 2020

## Slide 19: Part 3
Measures and Actions --what we are doing?

## Slide 20: Measures
●regulations and incentive policy
●Technology Advancement
●Demonstration projects
●Exploring and regulating markets
●International cooperation

## Slide 21: Policy Incentives
Subsides
directly subsides
  indirect subsides
Taxation
  half VAT for wind
  0 VAT for landfill power
  others
Financing
  Interest subsides
  National debt
  Development banks
  international banks

## Slide 22: Legislation/regulations/guidelines
  By 2004, draft RE promotion law
  Decrees
    New and renewable energy development plan for 1996-2010
    New and renewable energy industry development plan for the 10th five-year period
    Guidelines for wind energy industry development
    Guidelines for speeding up localization of wind turbines
    Currently developing guidelines for solar/biogas industrialization
    Start the developing the draft RE Promotion Law
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Mechanism Building
We are paying attentions to new mechanism for renewable energy:
  Wind concessional program
    2x100 MW wind farms
  Prepare renewable energy legislation
    RPS
    Feed in law, and
    Other
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Tech. Advancement/ demonstration projects
  Demonstrative wind farms to promote domestic 600kW wind turbine tech. Advancement
  Initiating pilot projects to integrate SWH into buildings
  SWH production tech. innovation projects
  Bagasse co-generation demonstration projects
  Demonstration projects for industrial/agricultural waste biogas engineering
  Hybrid village power system in Xinjiang
  Geothermal heat pump commercial demonstration projects
  ……

## Slide 25: Action Plans / Programs
National-bond Wind Power Program
  8 MW in 4 pilot projects
  Supporting the development of domestic wind turbine and component manufacture system
  National wind resources measure in total 10 wind farms
  Setting up the wind turbine certification program
Sunshine Industry Plan
  Promoting three industrial bases in Shandong, Jiangshu and Beijing
  Promoting 5-10 enterprises to expand their scales
  Using national bond to support enterprises’ technology advancements
  Promoting the integration of SWH into buildings

## Slide 26: Action Plans / Programs(cont.)
Western Sunshine Engineering
  Support solar industry development in western provinces (Xinjiang, Inner Mongolia, Qinghai, etc.)
  Support large-scale use of solar PV system for remote households
National Biogas Action Plan
  Under developing
  Supporting “three river basins” region to use biogas engineering technology to disposal water pollution

## Slide 27: International cooperation --Current Projects
1. SETC/WB/GEF RE project: China Renewable Energy Development Project
2. SETC/UNDP/GEF RE project: Capacity Building for the Rapid Commercialization of Renewable Energy in China
3. SETC/UNF Improvement and Expansion of Solar Water Heating Technology in China
4. Energy Foundation
5. SETC/ USDoE RE commercial business project/
Geothermal heat pump
6. Sino-EU Energy/Environment Project
7. others

## Slide 28: Thanks!